## Slide 1: 24-bit Audio CODEC
數位電路實驗
TA: 吳柏辰
Author: Trumen

## Slide 2: Outline
Introduction to Audio Signal
Architecture Overview
Device Initialization
Device Operation

## Slide 3: Introduction to Audio Signal

## Slide 4: Introduction
An audio signal = electrical voltage.
Headphones convert electrical signals into sound.
Microphones convert sound into electrical signals.
Audio signals have frequencies in the audio frequency range of roughly 20 to 20,000 Hz.

## Slide 5: Line In V.S. Mic In
Line input/output: 0.3 to 2 Volts.
Microphone input: 5 to 50 mV.
ADC is required to convert Voltage to 00101010

## Slide 6: Dual Channel
http://appleinsider.com/articles/09/02/12/macbook_owners_frustrated_by_new_audio_jacks

## Slide 7: Architecture Overview

## Slide 8
DE2_115_User_manual\DE2_115_User_manual.pdf

## Slide 9: Schematic Diagram
DE2_115_User_manual\DE2_115_User_manual.pdf

## Slide 10: Audio CODEC Pin Assignments
Signal Name | FPGA Pin No. | Description
I2C_SCLK | PIN_B7 | I2C Clock
I2C_SDAT | PIN_A8 | I2C Data
AUD_XCK | PIN_E1 | Audio CODEC Chip Clock
AUD_BCLK | PIN_F2 | Audio CODEC Bit-Steam Clock
AUD_ADCLRCK | PIN_C2 | Audio CODEC ADC LR Clock
AUD_ADCDAT | PIN_D2 | Audio CODEC ADC Data
AUD_DACLRCK | PIN_E3 | Audio CODEC DAC LR Clock
AUD_DACDAT | PIN_D1 | Audio CODEC DAC Data
DE2_115_User_manual\DE2_115_User_manual.pdf
Control
Data

## Slide 11: WM8731 Block Diagram
DE2_115_datasheets\Audio CODEC\WM8731.pdf

## Slide 12: How to Use WM8731?
Initialize the device by setting the registers via I2C bus interface.
After correct initialization, we can receive or transmit audio data via digital audio interface.

## Slide 13: Device Initialization

## Slide 14: I²C Protocol (1/4)
Data transfer in initiated with the START bit (S) when SDA is pulled low while SCL stays high.
Then, SDA sets the transferred bit while SCL is low (blue) and the data is sampled (received) when SCL rises (green).
SDA=1'b0

## Slide 15: I²C Protocol (2/4)
When the transfer is complete, a STOP bit (P) is sent by releasing the data line to allow it to be pulled up while SCL is constantly high.
In order to avoid false marker detection, the level on SDA is changed on the falling edge and is captured on the rising edge of SCL.
SDA=1'b1 or SDA=1'bz

## Slide 16: I²C Protocol (3/4)
After every 8 data bits in one direction, an "acknowledge" bit (0) is transmitted in the other direction.

## Slide 17: I²C Protocol (4/4)
Inout port example:
input in_dat;
input clk;
input out_enable;
output logic out_r;
logic out_w;
assign out_dat = out_enable ? out_r : 1’bz;
always_ff @(posedge clk) begin
out_r <= in_dat;
end

## Slide 18: Workable I²C Protocol
4/cycle bit, 1 ack bit/byte
3+3 cycles header
#Cycles is required for N-Bytes?
(This is not the full specification.)

## Slide 19: Software Control Interface (1/2)
Different modes can be configured under software control.
  Input to ADC: Microphone
  Sampling rate: 32kHz
  Input audio data bit length: 16 bits
  etc.

## Slide 20: 2-Wire Serial Control Mode
The WM8731/L supports a 2-wire MPU (Microprocessor unit) interface, which is compatible with I²C protocol.
  I²C (Inter-Integrated Circuit, referred to as I-squared-C) uses only two bidirectional open-drain lines, Serial Data Line (SDA) and Serial Clock (SCL).

## Slide 21: 2-Wire Interface (1/2)
The device operates as a slave device only.
The WM8731/L has one of two slave address that are selected by setting the state of the CSB pin.
CSB STATE | ADDRESS
0 | 0011010
1 | 0011011

## Slide 22: 2-Wire Interface (2/2)
2-wire serial interface
  ADDR[6:0] (7 bits) are Slave Address Bits
  R/W is '0', indicating a write
  B[15:9] (7 bits) are Register Address Bits
  B[8:0] (9 bits) are Register Data Bits
0011010
0
Max freq. = 526 kHz

## Slide 23: Register Map
Check the WM8731/L document to see the details.

## Slide 24: Digital Audio Interfaces
WM8731/L may be operated in either one of the 4 offered audio interface modes. These are:
  Right justified
  Left justified
  I2S
  DSP mode

## Slide 25: Digital Audio Interface Format
I2S format

## Slide 26: Digital Audio Interfaces
The length of the digital audio data is programmable at 16/20/24 or 32 bits.
The data is signed 2's complement.
  -32768~32767
  logic signed [15:0] dat;

## Slide 27: Digital Audio Interface Format
Master mode v.s. Slave mode

## Slide 28: Digital Audio Interface Format (1/2)
Choose I2S format, 16-bit length, and master mode.
  000_0111_0_0100_0010
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R7 (07h) Digital Audio Interface Format | 0 | BCLKIVE | MS | LRSWAP | LRP | IWL[[1:0] |  | FORMAT[1:0] |  | 0_0000_1010

## Slide 29: Recommended I²C Settings
Left Line In | 000_0000_0_1001_0111
Right Line In | 000_0001_0_1001_0111
Left Headphone Out | 000_0010_0_0111_1001
Right Headphone Out | 000_0011_0_0111_1001
Analogue Audio Path Control | 000_0100_0_0001_0101
Digital Audio Path Control | 000_0101_0_0000_0000
Power Down Control | 000_0110_0_0000_0000
Digital Audio Interface Format | 000_0111_0_0100_0010
Sampling Control | 000_1000_0_0001_1001
Active Control | 000_1001_0_0000_0001

## Slide 30: The End.
Any question?

## Slide 31: Reference
http://en.wikipedia.org/wiki/Audio_signal
http://en.wikipedia.org/wiki/I%C2%B2C
"THE I 2C-BUS SPECIFICATION VERSION 2.1" by Philips.
"DE2-115 User Manual" by Terasic.
"DE2-115_MB.pdf" by Terasic.
"WM8731.pdf" by Wolfson Microelectronics.

## Slide 32: Appendix

## Slide 33: Left Line In
Just use the default setting if we do not use the line input.
  000_0000_0_1001_0111
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R0 (00h) Left Line In | LRINBOTH | LINMUTE | 0 | 0 | LINVOL[4:0] |  |  |  |  | 0_1001_0111

## Slide 34: Right Line In
Just use the default setting if we do not use the line input.
  000_0001_0_1001_0111
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R1 (01h) Right Line In | RLINBOTH | RINMUTE | 0 | 0 | RINVOL[4:0] |  |  |  |  | 0_1001_0111

## Slide 35: Left Headphone Out
Here we can just use the default setting.
  000_0010_0_0111_1001
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R2 (02h) Left Headphone Out | LRHPBOTH | LZCEN | LHPVOL[6:0] |  |  |  |  |  |  | 0_0111_1001

## Slide 36: Right Headphone Out
Here we can just use the default setting.
  000_0011_0_0111_1001
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R3 (03h) Right Headphone Out | RLHPBOTH | RZCEN | RHPVOL[6:0] |  |  |  |  |  |  | 0_0111_1001

## Slide 37: Analogue Audio Path Control
Enable boost, disable mute, choose microphone input, disable bypass, and select DAC.
  000_0100_0_0001_0101
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R4 (04h) Analogue Audio Path Control | 0 | SIDEATT[1:0] |  | SIDETONE | DACSEL | BYPASS | INSEL | MUTEMIC | MICBOOST | 0_0000_1010

## Slide 38: Digital Audio Path Control
Disable soft mute
  000_0101_0_0000_0000
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R5 (05h) Digital Audio Path Control | 0 | 0 | 0 | 0 | HPOR | DACMU | DEEMPH[1:0] |  | ADCHPD | 0_0000_1000

## Slide 39: Power Down Control
Choose power on and disable all the power down options.
  000_0110_0_0000_0000
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R6 (06h) Power Down Control | 0 | POWER OFF | CLKOUTPD | OSCPD | OUTPD | DACPD | ADCPD | MICPD | LINEINPD | 0_1001_1111

## Slide 40: Digital Audio Interface Format (1/2)
Choose I2S format, 16-bit length, and master mode.
  000_0111_0_0100_0010
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R7 (07h) Digital Audio Interface Format | 0 | BCLKIVE | MS | LRSWAP | LRP | IWL[[1:0] |  | FORMAT[1:0] |  | 0_0000_1010

## Slide 41: Digital Audio Interface Format (2/2)
I2S format
Master mode v.s. Slave mode
16-bit length

## Slide 42: Sampling Control (1/2)
Choose USB mode (fixed MCLK 12MHz) and sampling rate = 32 kHz.
  000_1000_0_0001_1001
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R8 (08h) Sampling Control | 0 | CLKODIV2 | CLKIDIV2 | SR[3:0] |  |  |  | BOSR | USB/ Normal | 0_0000_0000

## Slide 43: Sampling Control (2/2)

## Slide 44: Active Control
Activate interface
  000_1001_0_0000_0001
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R9 (09h) Active Control | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Active | 0_0000_0000

## Slide 45: Reset Register
You can try to reset the device to a known (?) state.
  000_1111_0_0000_0000 (?)
REGISTER | BIT[8] | BIT[7] | BIT[6] | BIT[5] | BIT[4] | BIT[3] | BIT[2] | BIT[1] | BIT[0] | DEFAULT
R15 (15h) Active Control | RESET[8:0] |  |  |  |  |  |  |  |  | not reset